## Slide 1: 8085 Microprocessor
Dr. Manju Khurana
Assistant Professor, CSED
TIET, Patiala
manju.khurana@thapar.edu

## Slide 2: Instruction Formats
Each instruction has two parts:
Opcode (operation code)- The first part is the task or operation to be performed.
Operand - The second part is the data to be operated on. Data can be given in various forms.
  It can specify in various ways: may include 8 bit/16 bit data, an internal register, memory location or 8 bit /16 bit address.
  For Eg.:
  MVI A,02H
2
Introduction to Microprocessor Based Systems Design
Opcode
Operand

## Slide 3: Instruction word Size
An instruction is assembled in binary form (0,1) known as machine code or opcode. Due to different ways of specifying data or operand the machine code are not same for all the instructions.
The size of an instruction signifies how much memory space is required to load an instruction in the memory. 8085 instructions are of following sizes:
  One-byte or one word Instructions: opcode and operand in 8 bits
  only i.e. one byte. Operand(s) are internal register and are coded into the instruction.
  e.g. MOV, ADD, ANA, SUB, ORA etc.
MOV A,B Move the content of B in A
01 111 000 = 78H 01 for MOV operation, 111 binary code for register A and last 000 binary code for register B
3
Introduction to Microprocessor Based Systems Design

## Slide 4: Instruction Format or Size….Cont…
Two-byte instructions: first byte is opcode in 8 bits and second byte is operand either 8 bit data or 8 bit address.
e.g. MVI, ADI, ANI, ORI, XRI etc.
MVIB, 05H Move 05 to register B
06,05 MVIB, 05H in the code form
4
Introduction to Microprocessor Based Systems Design

## Slide 5: Instruction Format or Size….Cont…
Three-byte instructions: first byte is opcode in 8 bits and second and third byte are operand either 16 bit data or 16 bit address.
Operand 1 = lower 8 bit data/address
Operand 2 = Higher 8 bit data/address
opcode + data byte + data byte
e.g. LXI, LDA, STA, LHLD, SHLD etc.
LXIH , 2500H load HL pair with 2500H
21,00,25 LXIH , 2500H in code form
5
Introduction to Microprocessor Based Systems Design

## Slide 6: Addressing Modes
To perform any operation, we have to give the corresponding instructions to the microprocessor.
In each instruction, programmer has to specify 3 things:
  Operation to be performed.
  Address of source of data.
  Address of destination of result.
The method by which the address of source of data or the address of destination of result is given in the instruction is called Addressing Modes.
The term addressing mode refers to the way in which the operand of the instruction is specified.
6
Introduction to Microprocessor Based Systems Design

## Slide 7: Types of Addressing Modes
Intel 8085 uses the following addressing modes:
  Direct Addressing Mode
  Register Addressing Mode
  Register Indirect Addressing Mode
  Immediate Addressing Mode
  Implicit Addressing Mode
7
Introduction to Microprocessor Based Systems Design

## Slide 8: Direct Addressing Mode
In this mode, the address of the operand is given in the instruction itself.
LDA is the operation.
2500 H is the address of source.
Accumulator is the destination.
8
Introduction to Microprocessor Based Systems Design
LDA 2500 H | Load the contents of memory location 2500 H in accumulator.

## Slide 9: Register Addressing Mode
In this mode, the operand is in one of the general purpose register or accumulator.
MOV is the operation.
B is the source of data.
A is the destination.
9
Introduction to Microprocessor Based Systems Design
MOV A, B | Move the contents of register B to A.

## Slide 10: Register Indirect Addressing Mode
In this mode, the address of operand is specified by a register pair.
MOV is the operation.
M is the memory location specified by H-L register pair.
A is the destination.
10
Introduction to Microprocessor Based Systems Design
MOV A, M | Move data from memory location specified by H-L pair to accumulator.

## Slide 11: Immediate Addressing Mode
In this mode, the operand is specified within the instruction itself.
MVI is the operation.
05 H is the immediate data (source).
A is the destination.
11
Introduction to Microprocessor Based Systems Design
MVI A, 05 H | Move 05 H in accumulator.

## Slide 12: Implicit Addressing Mode
If address of source of data as well as address of destination of result is fixed, then there is no need to give any operand along with the instruction. It means there are certain instructions which operate on the content of the accumulator. Such instructions do not require the address of the operand.
CMA is the operation.
A is the source.
A is the destination.
12
Introduction to Microprocessor Based Systems Design
CMA | Complement accumulator.