## Slide 1: 8085 Microprocessor
Dr. Manju Khurana
Assistant Professor, CSED
TIET, Patiala
manju.khurana@thapar.edu

## Slide 2: Features of Microprocessor- 8085
8085 is developed by INTEL.
8 bit microprocessor: can accept 8 bit data simultaneously.
Operates on single +5V D.C. supply.
Designed using NMOS technology.
6200 transistor on a single chip.
It provides on chip clock generator, hence it does not require external clock generator.
Operates on 3MHz clock frequency.
8bit multiplexed address/data bus, which reduce the number of pins.
16address lines, hence it can address 2^16 = 64 K bytes of memory
It generates 8 bit I/O addresses, hence it can access 2^8 = 256 I/O ports.
5 hardware interrupts i.e. TRAP/RST4.5, RST 7.5, RST 6.5, RST 5.5, and INTR
It provides DMA (Direct memory access).
40-pin I.C. package fabricated on a single LSI chip.
Clock cycle is 320ns.
80 basic instructions and 246 opcodes.
Introduction to Microprocessor Based Systems Design

## Slide 3: Block Diagram of Intel 8085
3
Introduction to Microprocessor Based Systems Design

## Slide 4: Intel 8085 Architecture
8085 architecture consists of following blocks:
1. Register Array
2. ALU & Logical Group
3. Instruction decoder and machine cycle encoder, Timing and control circuitry
4. Interrupt control Group
5. Serial I/O control Group
4
Introduction to Microprocessor Based Systems Design

## Slide 5: Intel 8085 Architecture contd.
1. Registers Array :
General purpose register : (user accessible)
  B, C, D, E, H, L are 8 bit register. (can be used singly)
  Can also be used for 16-bit register pairs- BC, DE & HL.
  Used to store the intermediate data and result
  H & L can be used as a data pointer (holds memory address)
Special Purpose Register [A, Instruction Register and Flag]
(b.1) Accumulator (A) : (user accessible)
  8 bit register
  All the ALU operations are performed with reference to the contents of Accumulator.
  Result of an operation is stored in A.
  Store 8 bit data during I/O transfer
(b.2) Instruction Register: (user not accessible)
  When an instruction is fetched from memory, it is loaded in IR. Then transferred to the decoder for decoding.
  It is not programmable and can not be accessed through any instruction.
5
Introduction to Microprocessor Based Systems Design

## Slide 6: Intel 8085 Architecture contd.
(b.3) Flag Register (F) : (user accessible)
  8 bit Register
  Indicates the status of the ALU operation.
  ALU includes 5 flip flop, which are set or reset after an operation according to data conditions of the result in the accumulator.
6
Introduction to Microprocessor Based Systems Design

## Slide 7: Intel 8085 Architecture contd.
7
Introduction to Microprocessor Based Systems Design

## Slide 8: Intel 8085 Architecture contd.
(c) Temporary Register [ W, Z, Temporary data register]
  Internally used by the MP(user not accessible)
(c.1) W and Z register:
  8 bit capacity
  Used to hold temporary addresses during the execution of some instructions
  (c.2) Temporary data register:
  8 bit capacity
  Used to hold temporary data during ALU operations.
8
Introduction to Microprocessor Based Systems Design

## Slide 9: Intel 8085 Architecture contd.
(d) Pointer Register or special purpose [SP, PC]
(d.1) Stack Pointer (SP)
  16 bit address which holds the address of the data present at the top of the stack memory
  It is a reserved area of the memory in the RAM to store and retrieve the temporary information.
  Also hold the content of PC when subroutines are used.
  When there is a subroutine call or on an interrupt i.e. pushing the return address on a jump, and retrieving it after the operation is complete to come back to its original location.
(d.2) Program Counter (PC)
  16 bit address used for the execution of program
  Contain the address of the next instruction to be executed after fetching the instruction
  it is automatically incremented by 1.
  Not much use in programming, but as an indicator to user only.
9
Introduction to Microprocessor Based Systems Design

## Slide 10: Intel 8085 Architecture contd.
In addition to register MP contains some latches and buffer
Increment and decrement address latch
  16 bit register
  Used to increment or decrement the content of PC and SP
Address buffer
  8 bit unidirectional buffer
  Used to drive high order address bus(A8 to A15)
  When it is not used under such as reset, hold and halt etc this buffer is used tri-state high order address bus.
Data/Address buffer
  8 bit bi-Directional buffer
  Used to drive the low order address (A0 to A7) and data (D0 to D7) bus.
  Under certain conditions such as reset, hold and halt etc this buffer is used tri-state low order address bus.
10
Introduction to Microprocessor Based Systems Design

## Slide 11: Intel 8085 Architecture contd.
(2) ALU & Logical Group: it consists of ALU, Accumulator, Temporary register and Flag Register
ALU
  Performs arithmetic and logical operations
  Stores result of arithmetic and logical operations in accumulator
Accumulator
  General purpose register
  Stores one of the operand before any arithmetic and logical operations and result of operation is again stored back in Accumulator
  Store 8 bit data during I/O transfer
Temporary Register
  8 bit register
  During the arithmetic and logical operations one operand is available in A and other operand is always transferred to temporary register
  For Eg.: ADD B – content of B is transferred into temporary register before actual addition
Flag Register
  Five flags are connected to ALU
  After the ALU operation is performed the status of result will be stored in five flags.
11
Introduction to Microprocessor Based Systems Design

## Slide 12: Intel 8085 Architecture contd.
(3) Instruction decoder and machine cycle encoder, Timing and control circuitry
Instruction decoder and machine cycle encoder :
  Decodes the op-code stored in the Instruction Register (IR) and establishes the sequence of events to follow.
  Encodes it and transfer to the timing & control unit to perform the execution of the instruction.
Timing and control circuitry
  works as the brain of the CPU
  For proper sequence and synchronization of all the operations of MP, this unit generates all the timing and control signals necessary for communication between microprocessor and peripherals.
12
Introduction to Microprocessor Based Systems Design

## Slide 13: Intel 8085 Architecture contd.
(4) Interrupt Control group
Interrupt:- Occurrence of an external disturbance
  After servicing the interrupt, 8085 resumes its normal working sequence
  Transfer the control to special routines
  Five interrupts: - TRAP, RST7.5, RST6.5, RST5.5, INTR
  In response to INTR, it generates INTA signal
(5) Serial I/O control Group
  Data transfer D0- D7 lines is parallel data
  But under some conditions it is used serial data transfer
  Serial data is entered through SID (serial input data) input (received)
  Serial data is outputted on SOD (serial output data) input (send)
13
Introduction to Microprocessor Based Systems Design