## Slide 1: 8085 Microprocessor
Dr. Manju Khurana
Assistant Professor, CSED
TIET, Patiala
manju.khurana@thapar.edu

## Slide 2: Pin Diagram of Intel 8085
2
Introduction to Microprocessor Based Systems Design

## Slide 3: 8085 Pin Description
The 8085 is an 8-bit general purpose microprocessor that can address 64K Byte of memory.
It has 40 pins and uses +5V for power. It can run at a maximum frequency of 3 MHz.
The pins on the chip can be grouped into 9 groups:
  Address Bus and Data Bus
  Status Signals
  Control signal
  Interrupt signal
  Power supply and Clock signal
  Reset Signal
  DMA request Signal
  Serial I/O signal
  Externally Initiated Signals.
3
Introduction to Microprocessor Based Systems Design

## Slide 4: The Address and Data Busses
Address Bus (Pin 21-28)
  16 bit address lines A0 to A15
  The address bus has 8 signal lines A8 – A15 which are unidirectional.
  The other 8 address lines A0 to A7 are multiplexed (time shared) with the 8 data bits.
Data Bus (Pin 19-12)
  To save the number of pins lower order address pin are multiplexed with 8 bit data bus (bidirectional)
  So, the bits AD0 – AD7 are bi-directional and serve as A0 – A7 and D0 – D7 at the same time.
  During the execution of the instruction, these lines carry the address bits during the early part (T1 state), then during the late parts (T2 state) of the execution, they carry the 8 data bits.
4
Introduction to Microprocessor Based Systems Design

## Slide 5: Status Signals
Status Pins – ALE, S1, S0
ALE(Address Latch Enable) : (Pin 30)
  Used to demultiplexed the address and data bus
  +ve going pulse generated when a new operation is started by microprocessor.
  ALE = 1 when the AD0 – AD7 lines have an address
  ALE = 0 When it is low it indicates that the contents are data.
  This signal can be used to enable a latch to save the address bits from the AD lines.
S1 and S0 (Status Signal) : (Pin 33 and 29)
  Status signals to specify the kind of operation being performed .
  Usually un-used in small systems.
5
Introduction to Microprocessor Based Systems Design

## Slide 6: Control Signals
Control Pins – RD, WR, IO/M (active low)
RD: Read (Active low) (Pin 32)
  Read Memory or I/O device
  Indicated that data is to be read either from memory or I/P device and data bus is ready for accepting data from the memory or I/O device.
WR: Write (Active low) (Pin 31)
  Write Memory or I/O device
  Indicated that data on the data bus are to be written into selected memory or I/P device.
IO/M: (Input Output/Memory-Active low) (Pin 34)
  Signal specifies that the read/write operation relates to whether memory or I/O device.
  When (IO/M=1) the address on the address bus is for I/O device
  When (IO/M=0) the address on the address bus is for memory
6
Introduction to Microprocessor Based Systems Design

## Slide 7: Control and status Signals
When S0, S1 is combined with IO/M (active low), we get status of machine cycle
7
Introduction to Microprocessor Based Systems Design
Z= Tristate, X = don’t care condition

## Slide 8: Interrupts
They are the signals initiated by an external device to request the microprocessor to do a particular task or work.
There are five hardware interrupts called, (Pin 6-11)
On receipt of an interrupt, the microprocessor acknowledges the interrupt by the active low INTA (Interrupt Acknowledge) signal.
8
Introduction to Microprocessor Based Systems Design

## Slide 9: Power supply and Clock Signal
Vcc (Pin 40) : single +5 volt power supply
Vss (Pin 20) : Ground
X0 and X1 : (Pin 1-2)
  Crystal or R/C network or LC network connections to set the frequency of internal clock generator.
  The frequency is internally divided by two.
  Since the basic operating timing frequency is 3 MHz, a 6 MHz crystal is connected to the X0 and X1 pins.
CLK (output) : (Pin 37)
  Clock Output is used as the system clock for peripheral and devices interfaced with the microprocessor.
9
Introduction to Microprocessor Based Systems Design

## Slide 10: Reset Signals
Reset In (input, active low) (Pin 36)
  This signal is used to reset the microprocessor.
  The program counter inside the microprocessor is set to zero (0000H)
  The buses are tri-stated.
Reset Out (Output, Active High) (Pin 3)
  It indicates microprocessor is being reset.
  Used to reset all the connected devices when the microprocessor is reset.
10
Introduction to Microprocessor Based Systems Design

## Slide 11: DMA Request Signals
DMA:
  When 2 or more devices are connected to a common bus, to prevent the devices from interfering with each other, the tristate gates are used to disconnect all devices except the one that is communicating at a given instant .
  The CPU controls the data transfer operation between memory and I/O device.
  DMA operation is used for large volume data transfer between memory and an I/O device directly.
  The CPU is disabled by tri-stating its buses and the transfer is effected directly by external control circuits.
HOLD (Pin 38)
  This signal indicates that another device is requesting the use of address and data bus.
  So it relinquish the use of buses as soon as the current machine cycle is completed.
  Microprocessor regains the bus after the removal of a HOLD signal
HLDA (Pin 39)
  On receipt of HOLD signal, the MP acknowledges the request by sending out HLDA signal and leaves out the control of the buses.
  After the HLDA signal the DMA controller starts the direct transfer of data.
  After the removal of HOLD request HLDA goes low.
11
Introduction to Microprocessor Based Systems Design

## Slide 12: Serial I/O Signals
These pins are used for serial data communication
SID (input) Serial input data (Pin 4)
  It is a data line for serial input
  Used to accept serial data bit by bit from external device
  The data on this line is loaded into accumulator bit 7 whenever a RIM instruction is executed.
SOD (output) Serial output data (Pin 5)
  It is a data line for serial output
  Used to transmit serial data bit by bit to the external device
  The 7th bit of the accumulator is outputted on SOD line when SIM instruction is executed.
12
Introduction to Microprocessor Based Systems Design

## Slide 13: Externally Initiated signal
Ready (input) (Pin 35)
  Memory and I/O devices will have slower response compared to microprocessors.
  Before completing the present job such a slow peripheral may not be able to handle further data or control signals from CPU.
  The processor sets the READY signal after completing the present job to access the data.
  It synchronize slower peripheral to the processor.
  The microprocessor enters into WAIT state while the READY pin is disabled.
13
Introduction to Microprocessor Based Systems Design