## Slide 1: ADDRESSING MODES
Dr. Manju Khurana
Assistant Professor, CSED
TIET, Patiala
manju.khurana@thapar.edu

## Slide 2: Addressing Modes
Group I : Addressing modes for register and immediate data
Group II : Addressing modes for memory data
8086 Microprocessor
Every instruction of a program has to operate on a data.
The different ways in which a source operand is denoted in an instruction are known as addressing modes.
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement

## Slide 3: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
The instruction will specify the name of the register which holds the data to be operated by the instruction.
Example:
MOV CL, DH
The content of 8-bit register DH is moved to another 8-bit register CL
(CL)  (DH)
Group I : Addressing modes for register and immediate data

## Slide 4: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
In immediate addressing mode, an 8-bit or 16-bit data is specified as part of the instruction
Example:
MOV DL, 08H
The 8-bit data (08H) given in the instruction is moved to DL
(DL)  08H
MOV AX, 0A9FH
The 16-bit data (0A9FH) given in the instruction is moved to AX register
(AX)  0A9FH
Group I : Addressing modes for register and immediate data

## Slide 5: Addressing Modes : Memory Access
8086 Microprocessor
Physical Address (20 Bits)
Adder
Segment Register (16 bits)
0 0 0 0
Offset Value (16 bits)

## Slide 6: Addressing Modes : Memory Access
8086 Microprocessor
20 Address lines  8086 can address up to 220 = 1M bytes of memory
However, the largest register is only 16 bits
Physical Address will have to be calculated Physical Address : Actual address of a byte in memory. i.e. the value which goes out onto the address bus.
Memory Address represented in the form – Seg : Offset (Eg - 89AB:F012)
Each time the processor wants to access memory, it takes the contents of a segment register, shifts it one hexadecimal place to the left (same as multiplying by 1610), then add the required offset to form the 20- bit address
89AB : F012  89AB  89AB0 (Paragraph to byte  89AB x 10 = 89AB0)
F012  0F012 (Offset is already in byte unit)
+ -------
98AC2 (The absolute address)
16 bytes of contiguous memory

## Slide 7: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
In direct addressing mode the operand’s offset is given in the instruction as an 8-bit or 16-bit displacement element.
Examples are:
MOV BX, [1354H]
MOV BL, [0400H]
The square brackets around the 1354H denotes the contents of the memory location. When executed, this instruction will copy the contents of the memory location into BX register.
This addressing mode is called direct because the displacement of the operand from the segment base is specified directly in the instruction.

## Slide 8: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
In Register indirect addressing, operand’s offset is placed in any one of the registers BX, BP, SI or DI as specified in the instruction.
Example:
MOV CX, [BX]
ADD AL, [SI]

## Slide 9: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
In Based Addressing, operand’s offset is the sum of an 8-bit or 16-bit displacement and the contents of the base register BX or BP. BX is used as a base register for data segment, and BP is used as a base register for stack segment.
Offset (Effective address)= [BX + 8-bit or 16-bit displacement]
Examples are:
MOV AL, [BX + 05H]
MOV AL, [BX + 1346H]

## Slide 10: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
The operand’s offset is the sum of the content of an index register SI or DI and an 8-bit or 16-bit displacement.
Offset (Effective address)= [SI or DI + 8-bit or 16-bit displacement]
MOV AX, [SI + 05]
MOV AX, [SI + 1528H]

## Slide 11: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
In Based Index Addressing, the operand’s offset is the sum of the content of a base register BX or BP and an index register SI or DI.
Offset (Effective address)= [BX or BP]+ [SI or DI]
Examples are:
ADD AX, [BX + SI]
MOV CX, [BX + SI]

## Slide 12: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Indexed Addressing
Based Indexed with Displacement
Group II : Addressing modes for memory data
In this mode of addressing the operand’s offset is given by
    Offset (Effective address)= [BX or BP]+ [SI or DI] + 8-bit or 16-bit displacement
    Examples are:
    MOV AX, [BX + SI + 05]
    MOV AX, [BX + SI + 1235H]